## Slide 1: MicroPython: The Next Steps to World Domination
Steve Holden
CTO, Global Stress Index Limited

## Slide 2: Introductions
Started programming in 1968
Computational scientist by training
Engineer at heart, electronics hobbyist
Python user since Python 1.4
Enjoy helping people to learn

## Slide 3: 1948
Notes: 1.1KIPS == 0.0011 MMIPS (A thousandth of a MIPS)

## Slide 4: 1977
Notes: VAX 11/780 = 1 MIPS

## Slide 5: 1984
Notes: 0.52 MIPS (36 years)

## Slide 6: 2015

## Slide 7: 2016
Notes: 200 MIPS!!!!

## Slide 8: 2017
Notes: FiPy: Five networks: WiFi, Bluetooth, LORA, SigFox, LTE
ESP32: Wifi plus huge resources and 600 DMIPS!

## Slide 9: Some ESP32 Features
Twin-core CPU (200 MIPS)
Wifi and Bluetooth
Crypto acceleration
Touch sensing
A-to-D and D-to-A
Many comms interfaces

## Slide 10: 2020
?
Notes: Who knows where we are going? These are crazy times!

## Slide 11: 20-Year Plan for World Domination
Help grow Python’s communities
Help underpin the Python Software Foundation
Profit? (and for whom?)
A million new users in a single year might help…

## Slide 12: A Seminal Moment: 22.03.2016
Notes: Date: 22.03.2016 Last updated: 29.03.2016 at 08.12
Category: Make It Digital
In a landmark moment, from today up to one million BBC micro:bits are being delivered free to every year 7 student in England and Wales, year 8 student in Northern Ireland and S1 student in Scotland. The BBC micro:bit, launched as part of the BBC Make it Digital initiative, is a pocket-sized codeable computer that allows young people to get creative with technology, whatever their level of experience, and aims to help develop a new generation of digital pioneers.

## Slide 13: Goal: Python in Everyone’s Reach

## Slide 14: Note to Purists
We are talking about learners
They do not need huge libraries
Direct hands-on experience enables
Large resources are not required
  Large numbers of devices are

## Slide 15: MicroPython
Damien George
Nick Tollervey
Notes: Damien George, inventor of MicroPyhton
Nick Tollervey, developer of mu

## Slide 16: MicroPython Features
The entire Python 3.4 syntax, including
  Exceptions
  with , yield from, etc.
Also adds 3.5’s async and await
Optional machine code!
Types include str, bytes, bytearray, tuple, list, dict, set, frozenset, array.array, collections.namedtuple
Also, naturally, classes and instances

## Slide 17: Supported Systems
PyBoard
WiPy
ESP8266
ESP32
STM32F4
NUCLEO boards
Espruino Pico

## Slide 18: Filesystem
A small amount of EPROM appears as /flash
With hardware support you can also get /sd
  One or the other becomes current directory
Can access via an abbreviated os module
open works as usual

## Slide 19: Boot Sequence
boot.py is run
The USB interface is enabled
main.py is run
Most systems also allow a safe-mode boot
  Helpful when you get boot.py wrong
Can reset the filesystem to factory settings

## Slide 20: Paste Mode
Enter with ^E
Paste code in
Terminate entry and parse code with ^D

## Slide 21: Commercial Support

## Slide 22: Zerynth MicroPython Features
Studio: an IDE
VM: real-time ‘OS’ – hardware independent
Advanced Device Manager
  OTA updates and remote procedure calls
App: mobile phones to communicate directly with Python-programmed IoT things

## Slide 23: Zerynth Supported Systems
ESP8266
ESP32
Microchip/Atmel SAM*
Nordic NRF*
NXP K64
Particle Photon
33 different systems in all!

## Slide 24: Digital I/O
from machine import Pin
# Digital input
in_pin = Pin(0, machine.Pin.IN, machine.Pin.PULL_UP)
p = in_pin.value()
# Digital output
out_pin = machine.Pin(0, machine.Pin.OUT)
# Set of clear using the same method
out_pin.value(1) # sets it
Out_pin.value(0) # clears it

## Slide 25: File Handling
# Files are stored in a FAT filesystem in flash memory
>>> f = open('data.txt', 'w')
>>> f.write('some data')
9
>>> f.close()
>>> f = open('data.txt')
>>> f.read()
'some data'
>>> f.close()

## Slide 26: Simple Networking
def http_get(url):
_, _, host, path = url.split('/', 3)
addr = socket.getaddrinfo(host, 80)[0][-1]
s = socket.socket()
s.connect(addr)
s.send(bytes('GET /%s HTTP/1.0\r\nHost: %s\r\n\r\n' % (path, host), 'utf8'))
while True:
data = s.recv(100)
if data:
print(str(data, 'utf8'), end='')
else:
break
s.close()

## Slide 27: Hobby Servomotor Control
import pyb
s1 = pyb.Servo(1) # create a servo object on position X1
s2 = pyb.Servo(2) # create a servo object on position X2
s1.angle(45) # move servo 1 to 45 degrees
s2.angle(0) # move servo 2 to 0 degrees
# move servo1 and servo2 synchronously, taking 1500ms
s1.angle(-60, 1500)
s2.angle(30, 1500)

## Slide 28: Interrupt Handling
>>> def callback(p):
... print('pin change', p)
>>> from machine import Pin
>>> p0 = Pin(0, Pin.IN)
>>> p2 = Pin(2, Pin.IN)
>>> p0.irq(trigger=Pin.IRQ_FALLING, handler=callback)
>>> p2.irq(trigger=Pin.IRQ_RISING | Pin.IRQ_FALLING, handler=callback)

## Slide 29: Power Control
import machine
# configure RTC.ALARM0 to be able to wake the device
rtc = machine.RTC()
rtc.irq(trigger=rtc.ALARM0, wake=machine.DEEPSLEEP)
# set RTC.ALARM0 to fire after 10 seconds (waking the device)
rtc.alarm(rtc.ALARM0, 10000)
# put the device to sleep
machine.deepsleep()
...
if machine.reset_cause() == machine.DEEPSLEEP_RESET:
print('woke from a deep sleep')
else:
print('power on or hard reset')

## Slide 30: www.micropython.org/unicorn/

## Slide 31: A Real-world problem
De-bouncing switches

## Slide 32: Switches Aren’t Just On/Off

## Slide 33: Solving The Problem
Use a pure software solution
  Sample at regular intervals
  Switch is stable when N samples are the same

## Slide 34: Switch Class Definition
from machine import Timer, Pin
class Switch:
def __init__(self, pin_no, name):
self._state = 0
self.value = 0
self.pin = Pin(pin_no)
self.name = name
def output(self):
"Return name of switch if closed, dot if open."
return self.name if self.value else "."

## Slide 35: Debouncer Class Definition (1)
class Debouncer:
def __init__(self):
self.switches = []
self.timer = Timer(-1)
self.timer.init(period=6, mode=Timer.PERIODIC, callback=self.tick)
def register(self, switch):
"Add a switch to the bank."
self.switches.append(switch)
switch.pin.init(mode=Pin.IN, pull=Pin.PULL_UP)
return switch
6 ms intervals

## Slide 36: Debouncer Class Definition (2)
def tick(self, _):
"Examine input states and note debounced state changes."
for switch in self.switches:
bit = switch.pin.value()
switch._state = ((switch._state << 1) | bit) & 0xfff
# Latch state if last 12 samples were equal
if switch._state == 0x000: # switch pressed
switch.value = True
elif switch._state == 0xfff: # switch released
switch.value = False

## Slide 37: Switch Setup on ESP8266
def switches():
"Report names of closed switches."
return "".join(x.output() for x in (R, W, B, Y))
# Create a bank of four debounced switches
d = Debouncer()
Y = d.register(Switch(0, "Y")) # D3
R = d.register(Switch(14, "R")) # D5
W = d.register(Switch(12, "W")) # D6
B = d.register(Switch(13, "B")) # D7

## Slide 38: Main Loop
# Background task loops reporting changes in any switch's state
state = switches()
while True:
new_state = switches()
if new_state != state:
state = new_state
print(state)

## Slide 39: Installation (ESP8266 Systems)
wget http://micropython.org/resources/firmware/esp8266-20170823-v1.9.2.bin
pip install esptool
alias esptool="python -m esptool --port /dev/tty.wchusbserial1410"
esptool erase_flash
esptool --baud 115200 write_flash --flash_size=detect 0 \
esp8266-20170823-v1.9.2.bin

## Slide 40: Live Demonstration!

## Slide 41: Possibilities …
Robot control
Toys and games
Weather stations
Light patterns
Science instrumentation/data collection

## Slide 42: Final Thoughts
Computers don’t just belong in mathematics
MicroPython gives children direct, hands-on experience
  Puts them in control
The younger they start, the more useful they will find computers

## Slide 43: Questions?
Contact me:
sh@felix.com
@holdenweb
Slides and code available at
http://github.com/holdenweb/PyConIE2017

## Slide 44: More Resources
github.com/micropython/
github.com/micropython/micropython/wiki
www.micropython.org/download
twitter.com/search?q=#micropython